Network Working Group                                       B. Lourdelet

Internet-Draft                                               W. Dec, Ed.

Intended status: Standards Track                     Cisco Systems, Inc.

Expires: September 15, 2011                                  B. Sarikaya

Huawei USA

G. Zorn

Network Zen

D. Miles

Alcatel-Lucent

March 14, 2011

RADIUS attributes for IPv6 Access Networks

draft-ietf-radext-ipv6-access-04.txt

Abstract

This document specifies additional IPv6 RADIUS attributes useful in

residential broadband network deployments.  The attributes, which are

used for authorization and accounting, enable assignment of a host

IPv6 address and IPv6 DNS server address via DHCPv6; assignment of an

IPv6 route announced via router advertisement, assignment of a

named IPv6 delegated prefix pool and assignment of a named IPv6 pool for DHCPv6 based addressing, when a single IPv6 address needs to be assigned to a host.

Requirements Language

The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT",

"SHOULD", "SHOULD NOT", "RECOMMENDED", "MAY", and "OPTIONAL" in this

document are to be interpreted as described in RFC 2119 [RFC2119].

Status of this Memo

This Internet-Draft is submitted in full conformance with the

provisions of BCP 78 and BCP 79.

Internet-Drafts are working documents of the Internet Engineering

Task Force (IETF).  Note that other groups may also distribute

working documents as Internet-Drafts.  The list of current Internet-

Drafts is at http://datatracker.ietf.org/drafts/current/.

Internet-Drafts are draft documents valid for a maximum of six months

and may be updated, replaced, or obsoleted by other documents at any

time.  It is inappropriate to use Internet-Drafts as reference

material or to cite them other than as "work in progress."

This Internet-Draft will expire on September 15, 2011.

Copyright Notice

Lourdelet, et al.      Expires September 15, 2011               [Page 1]

Internet-Draft             RADIUS IPv6 Access                 March 2011

Copyright (c) 2011 IETF Trust and the persons identified as the

document authors.  All rights reserved.

This document is subject to BCP 78 and the IETF Trust's Legal

Provisions Relating to IETF Documents

(http://trustee.ietf.org/license-info) in effect on the date of

publication of this document.  Please review these documents

carefully, as they describe your rights and restrictions with respect

to this document.  Code Components extracted from this document must

include Simplified BSD License text as described in Section 4.e of

the Trust Legal Provisions and are provided without warranty as

described in the Simplified BSD License.

This document may contain material from IETF Documents or IETF

Contributions published or made publicly available before November

10, 2008.  The person(s) controlling the copyright in some of this

material may not have granted the IETF Trust the right to allow

modifications of such material outside the IETF Standards Process.

Without obtaining an adequate license from the person(s) controlling

the copyright in such materials, this document may not be modified

outside the IETF Standards Process, and derivative works of it may

not be created outside the IETF Standards Process, except to format

it for publication as an RFC or to translate it into languages other

than English.

Lourdelet, et al.      Expires September 15, 2011               [Page 2]

Internet-Draft             RADIUS IPv6 Access                 March 2011

Table of Contents

1.  Introduction . . . . . . . . . . . . . . . . . . . . . . . . .  4

2.  Deployment Scenarios . . . . . . . . . . . . . . . . . . . . .  4

2.1.  IPv6 Address Assignment  . . . . . . . . . . . . . . . . .  5

2.2.  Recursive DNS Servers  . . . . . . . . . . . . . . . . . .  6

2.3.  IPv6 Route Information . . . . . . . . . . . . . . . . . .  6

2.4.  Delegated IPv6 Prefix Pool . . . . . . . . . . . . . . . .  6

3.  Attributes . . . . . . . . . . . . . . . . . . . . . . . . . .  7

3.1.  Framed-IPv6-Address  . . . . . . . . . . . . . . . . . . .  7

3.2.  DNS-Server-IPv6-Address  . . . . . . . . . . . . . . . . .  8

3.3.  Route-IPv6-Information . . . . . . . . . . . . . . . . . .  9

3.4.  Delegated-IPv6-Prefix-Pool . . . . . . . . . . . . . . . . 10

3.5.  Table of attributes  . . . . . . . . . . . . . . . . . . . 10

4.  Diameter Considerations  . . . . . . . . . . . . . . . . . . . 10

5.  Security Considerations  . . . . . . . . . . . . . . . . . . . 11

6.  IANA Considerations  . . . . . . . . . . . . . . . . . . . . . 11

7.  Acknowledgements . . . . . . . . . . . . . . . . . . . . . . . 11

8.  References . . . . . . . . . . . . . . . . . . . . . . . . . . 11

8.1.  Normative References . . . . . . . . . . . . . . . . . . . 11

8.2.  Informative References . . . . . . . . . . . . . . . . . . 12

Authors' Addresses . . . . . . . . . . . . . . . . . . . . . . . . 12

Lourdelet, et al.      Expires September 15, 2011               [Page 3]

Internet-Draft             RADIUS IPv6 Access                 March 2011

1.  Introduction

In IPv6 deployments DHCPv6 and/or ICMPv6 Router Advertisements can be

used to convey configuration information by a NAS towards accessing

hosts.  Such information typically needs to be provisioned on the NAS

and may be done so on a per host or user basis using the AAA process.

This document specifies additional RADIUS attributes used to support

configuration of DHCPv6 and/or ICMPv6 parameters on a per-user basis.

The attributes, which complement those defined in [RFC3162] and

[RFC4818], support the following:

o  The assignment or accounting of specific IPv6 addresses assigned

to hosts.  While [RFC3162] permits an IPv6 address to be specified

via the combination of the Framed-Interface-Id and Framed-IPv6-

Prefix attributes, this separation is more natural for use with

IPv6CP than it is for use with DHCPv6, and the use of a single

IPv6 address attribute makes for easier processing of accounting

records.

o  Assignment of an IPv6 DNS server address, via DHCPv6 or [RFC5006]

o  Configuration of a route to be passed to the host via Router

Advertisement [RFC4191] or other similar mechanisms (eg DHCPv6)

o  The assignment of a named delegated prefix pool for use with "IPv6

Prefix Options for DHCPv6" [RFC3633]

- The assignment of a named IPv6 pool for DHCPv6 based addressing, when a single IPv6 address needs to be assigned to a host for the same reasons described in the first bullet.

2.  Deployment Scenarios

A common broadband network scenario is illustrated in Figure 1.  It

is composed of a IP Routing Residential Gateway (RG) or host, a Layer

2 Access-Node (e.g. a DSLAM), one or more IP Network Access Servers

(NASes), and an AAA server.  The RG or host are expected to be multi

homed to both NASes.  Layer 2 Connectivity between the host and NAS

can be either via PPPoE or IP over Ethernet, and established

dynamically.

Lourdelet, et al.      Expires September 15, 2011               [Page 4]

Internet-Draft             RADIUS IPv6 Access                 March 2011

+-----+

(Radius)   | AAA |

...........>|     |

.           +--+--+

v              ^

+---+---+          .

|  NAS  |          .(Radius)

|       |          .

+---+---+          v

+------+           |          +---+---+

+------+       |  AN  |           |          |  NAS  |

|  RG/ +-------|      +-----------+----------+       |

| host |       |      |                      |       |

+------+ (DSL) +------+      (Ethernet)      +-------+

Figure 1

In this scenario the NASes may embed a DHCPv6 server to handle DHCPv6

requests issued by RGs/hosts, as well as acting as a router providing

Router Advertisements.  The RADIUS server authenticates each RG/host

and returns to the NAS attributes used for authorization and

accounting.  These attributes can include a host IPv6 address to be

configured via DHCPv6; the IPv6 address of a DNS server to configured

via DHCPv6 or router advertisement; the name of a prefix pool to be

used for DHCPv6 Prefix Delegation; or IPv6 routes to be announced to

the host.

The following sub-sections discuss how these uses in more detail.

2.1.  IPv6 Address Assignment

DHCPv6 [RFC3315] provides a mechanism to assign one or more or non-

temporary IPv6 addresses to hosts.  To provide a DHCPv6 server

residing on a NAS with one or more IPv6 addresses to be assigned,

this document specifies the Framed-IPv6-Address Attribute.

Since DHCPv6 can be deployed on the same network as ICMPv6 stateless

(SLAAC) [RFC4862], it is possible that the NAS will require both

stateful and stateless configuration information.  Therefore it is

possible for the Framed-IPv6-Address, Framed-IPv6-Prefix and Framed-

Interface-Id attributes [RFC3162] to be included within the same

packet.  To avoid ambiguity, the Framed-IPv6-Address attribute is

only used for authorization and accounting of DHCPv6-assigned

addresses and the Framed-IPv6-Prefix and Framed-Interface-Id

attributes are used for authorization and accounting of addresses

assigned via SLAAC.

Lourdelet, et al.      Expires September 15, 2011               [Page 5]

Internet-Draft             RADIUS IPv6 Access                 March 2011

2.2.  Recursive DNS Servers

DHCPv6 provides an option for recursive DNS servers to hosts, as does

ICMPv6 with Router Advertisements supporting the experimental

[RFC5006] option.  Existing IETF RADIUS attributes convey DNS as 32-

bit IPv4 addresses and cannot support a 128-bit IPv6 address.  This

document specifies the RADIUS attribute to convey a list of IPv6 DNS

Recursive name server addresses, from an AAA server, which can that

can be conveyed by a NAS to a host.

2.3.  IPv6 Route Information

An IPv6 Route Information option, defined in [RFC4191] is intended to

be used to inform a host connected to the NAS that a specific route

is reachable via the NAS.  This is particularly desirable in cases

where the RG or host are multi-homed to different NASes as shown in

Figure 1.

This document specifies the RADIUS attribute that allows the AAA

system to provision the announcement by the NAS of a specific Route

Information Option to an accessing host.  The NAS may advertise this

route using the method defined in [RFC4191] or using other equivalent

methods.

The distinction and separation between this attribute and the Framed-

IPv6-Route attribute defined in [RFC3162] is needed due to the need

to have the information carried by this attribute advertised (in

binary format as per RFC4191) to an attaching client, rather than

intended for the NAS itself.

2.4.  Delegated IPv6 Prefix Pool

DHCPv6 Prefix Delegation [RFC3633] involves a delegating router

selecting a prefix and delegating it on a temporary basis to a

requesting router.  The delegating router may implement a number of

strategies as to how it chooses what prefix is to be delegated to a

requesting router, one of them being the use of a local named prefix

pool.  The Delegated-IPv6-Prefix-Pool Attribute allows the RADIUS

server to convey a prefix pool name to a NAS hosting a DHCPv6-PD

server and acting as a delegated router.

Since DHCPv6 Prefix Delegation can conceivably be used on the same

network as SLAAC, it is possible for the Delegated-IPv6-Prefix-Pool

and Framed-IPv6-Pool attributes to be included within the same

packet.  To avoid ambiguity in this scenario, use of the Delegated-

IPv6-Prefix-Pool attribute should be restricted to authorization and

accounting of prefix pools used in DHCPv6 Prefix Delegation and the

Framed-IPv6-Pool attribute should be used for authorization and

Lourdelet, et al.      Expires September 15, 2011               [Page 6]

Internet-Draft             RADIUS IPv6 Access                 March 2011

accounting of prefix pools used in SLAAC.

2.5 IPv6 pool for DHCPv6 address assignment

DHCPv6 [RFC3315] provides a mechanism to assign one or more or non-

temporary IPv6 addresses to hosts.  Section 2.1 introduces Framed-IPv6-Address Attribute to be used for providing a DHCPv6 server residing on a NAS with one or more IPv6 addresses to be assigned to the clients. An alternative way to achieve a similar result is to extract an IPv6 address to be assigned, from a pool locally configured on the NAS. This document specifies the DHCPv6-IPv6-Address-Pool attribute to allow the RADIUS server to convey a pool name to be used for DHCPv6 based addressing, when a single IPv6 address needs to be assigned to a host, to a NAS hosting a DHCPv6 server.

Since DHCPv6 can conceivably be used on the same network as DHCPv6 Prefix Delegation, it is possible for the Delegated-IPv6-Prefix-Pool

and DHCPv6-IPv6-Address-Pool attributes to be included within the same

packet.  To avoid ambiguity in this scenario, use of the Delegated-

IPv6-Prefix-Pool attribute should be restricted to authorization and

accounting of prefix pools used in DHCPv6 Prefix Delegation and the

DHCPv6-IPv6-Address-Pool attribute should be used for authorization and accounting of IPv6 address pool used for DHCPv6 based addressing when a single IPv6 address needs to be assigned to a link.

3.  Attributes

The fields shown in the diagrams below are transmitted from left to

right.

3.1.  Framed-IPv6-Address

This Attribute indicates an IPv6 Address that is assigned to the NAS-

facing interface of the RG/host.  It MAY be used in Access-Accept

packets, and MAY appear multiple times.  It MAY be used in an Access-

Request packet as a hint by the NAS to the server that it would

prefer these IPv6 address(es), but the server is not required to

honor the hint.  Since it is assumed that the NAS will add a route

corresponding to the address, it is not necessary for the server to

also send a host Framed-IPv6-Route attribute for the same address.

This Attribute can be used by a DHCPv6 process on the NAS to assign a

unique IPv6 address to the RG/host.

A summary of the Framed-IPv6-Address Attribute format is shown below.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|     Type      |     Length    |            Address

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Address (cont)

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Address (cont)

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Address (cont)

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Address (cont.)        |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Type

TBA1 for Framed-IPv6-Address

Length

18

Lourdelet, et al.      Expires September 15, 2011               [Page 7]

Internet-Draft             RADIUS IPv6 Access                 March 2011

Address

The IPv6 address field contains a 128-bit IPv6 address.

3.2.  DNS-Server-IPv6-Address

The DNS-Server-IPv6-Address Attribute contains the IPv6 address of a

recursive DNS server.  This attribute MAY be included multiple times

in Access-Accept packets, when the intention is for a NAS to announce

more than one recursive DNS address to an RG/host.  The same order of

the attributes is expected to be followed in the announcements to the

client.

The content of this attribute can be inserted in a DHCPv6 option as

specified in [RFC3646] or mapped option.

A summary of the DNS-Server-IPv6-Address Attribute format is given

below.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|     Type      |     Length    |            Address

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Address (cont)

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Address (cont)

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Address (cont)

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Address (cont.)        |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Type

TBA2 for DNS-Server-IPv6-Address

Length

18

Address

The 128-bit IPv6 address of a DNS server.

Lourdelet, et al.      Expires September 15, 2011               [Page 8]

Internet-Draft             RADIUS IPv6 Access                 March 2011

3.3.  Route-IPv6-Information

This Attribute specifies a prefix (and corresponding route) to be

authorized for announcement towards the user by the NAS, with the

reachable by means of routing towards the NAS.  It is used in the

Access-Accept packet and can appear multiple times.  It may also be

used in the Access-Request packet as hint to the server.

A summary of the Route-IPv6-Information attribute format is shown

below.  The route information option defined in [RFC4191] is captured

in this and following two attributes.

0                   1                   2                   3

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|     Type      |    Length     |   Reserved    | Prefix-Length |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|                                                               |

.                        Prefix (variable)                      .

.                                                               .

|                                                               |

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Type

TBA3 for Route-IPv6-Information

Length

Length in bytes.  At least 4 and no larger than 20; typically 12

or less.

Prefix Length

The length of the prefix, in bits; at least 0 and no more than

128; typically 64 or less.

Prefix

Variable-length field containing an IP prefix.  The Prefix Length

field contains the number of valid leading bits in the prefix.

The bits in the prefix after the prefix length (if any) up to the

byte boundary are reserved and MUST be initialized to zero by the

sender and ignored by the receiver.

Lourdelet, et al.      Expires September 15, 2011               [Page 9]

Internet-Draft             RADIUS IPv6 Access                 March 2011

3.4.  Delegated-IPv6-Prefix-Pool

This Attribute contains the name of an assigned pool that SHOULD be

used to select an IPv6 delegated prefix for the user.  If a NAS does

not support multiple prefix pools, the NAS MUST ignore this

Attribute.

A summary of the Delegated-IPv6-Prefix-Pool Attribute format is shown

below.  The fields are transmitted from left to right.

0                   1                   2

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|     Type      |    Length     |     String...

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Type

TBA4 for Delegated-IPv6-Prefix-Pool

Length

Length in bytes.  At least 4.

String

The string field contains the name of an assigned IPv6 prefix pool

configured on the NAS.  The field is not NULL (hex 00) terminated.

3.5.  DHCPv6-IPv6-Address-Pool

This Attribute contains the name of an assigned pool that SHOULD be

used to select an IPv6 address for the user.  If a NAS does

not support multiple prefix pools, the NAS MUST ignore this

Attribute.

A summary of the DHCPv6-IPv6-Address-Pool Attribute format is shown

below.  The fields are transmitted from left to right.

0                   1                   2

0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

|     Type      |    Length     |     String...

+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

Type

TBA4 for DHCPv6-IPv6-Address-Pool

Length

Length in bytes.  At least 4.

String

The string field contains the name of an assigned IPv6 address pool

configured on the NAS.  The field is not NULL (hex 00) terminated.

3.5.  Table of attributes

The following table provides a guide to which attributes may be found

in which kinds of packets, and in what quantity.

Request Accept Reject Challenge Accounting    #  Attribute

Request

0+      0+     0      0         0+      TBA1  Framed-IPv6-Address

0+      0+     0      0         0+      TBA2  DNS-Server-IPv6-Address

0       0+     0      0         0+      TBA3  Route-IPv6-Information

0      0-1     0      0        0-1      TBA4  Delegated-IPv6-Prefix-Pool

0      0-1     0      0        0-1      TBA4  DHCPv6-IPv6-Address-Pool

4.  Diameter Considerations

Given that the Attributes defined in this document are allocated from

the standard RADIUS type space (see Section 6), no special handling

is required by Diameter entities.

Lourdelet, et al.      Expires September 15, 2011              [Page 10]

Internet-Draft             RADIUS IPv6 Access                 March 2011

5.  Security Considerations

This document describes the use of RADIUS for the purposes of

authentication, authorization and accounting in IPv6-enabled

networks.  In such networks, the RADIUS protocol may run either over

IPv4 or over IPv6.  Known security vulnerabilities of the RADIUS

protocol apply to the attributes defined in this document.  Since

IPSEC is natively defined for IPv6, it is expected that running

RADIUS implementations supporting IPv6 may want to run over IPSEC.

Where RADIUS is run over IPSEC and where certificates are used for

authentication, it may be desirable to avoid management of RADIUS

shared secrets, so as to leverage the improved scalability of public

key infrastructure.

6.  IANA Considerations

This document requires the assignment of three new RADIUS Attribute

Types in the "Radius Types" registry (currently located at

http://www.iana.org/assignments/radius-types for the following

attributes:

o  Framed-IPv6-Address

o  DNS-Server-IPv6-Address

o  Route-IPv6-Information

- Delegated-IPv6-Prefix-Pool

- DHCPv6-IPv6-Address-Pool

7.  Acknowledgements

The authors would like to thank Bernard Aboba, Alfred Hines, Alan

DeKok, Peter Deacon, and Mark Smith for their help and comments in

reviewing this document.

8.  References

8.1.  Normative References

[RFC2119]  Bradner, S., "Key words for use in RFCs to Indicate

Requirement Levels", BCP 14, RFC 2119, March 1997.

[RFC4862]  Thomson, S., Narten, T., and T. Jinmei, "IPv6 Stateless

Address Autoconfiguration", RFC 4862, September 2007.

Lourdelet, et al.      Expires September 15, 2011              [Page 11]

Internet-Draft             RADIUS IPv6 Access                 March 2011

8.2.  Informative References

[RFC3162]  Aboba, B., Zorn, G., and D. Mitton, "RADIUS and IPv6",

RFC 3162, August 2001.

[RFC3315]  Droms, R., Bound, J., Volz, B., Lemon, T., Perkins, C.,

and M. Carney, "Dynamic Host Configuration Protocol for

IPv6 (DHCPv6)", RFC 3315, July 2003.

[RFC3633]  Troan, O. and R. Droms, "IPv6 Prefix Options for Dynamic

Host Configuration Protocol (DHCP) version 6", RFC 3633,

December 2003.

[RFC3646]  "".

[RFC4191]  Draves, R. and D. Thaler, "Default Router Preferences and

More-Specific Routes", RFC 4191, November 2005.

[RFC4818]  Salowey, J. and R. Droms, "RADIUS Delegated-IPv6-Prefix

Attribute", RFC 4818, April 2007.

[RFC4861]  Narten, T., Nordmark, E., Simpson, W., and H. Soliman,

"Neighbor Discovery for IP version 6 (IPv6)", RFC 4861,

September 2007.

[RFC5006]  Jeong, J., Park, S., Beloeil, L., and S. Madanapalli,

"IPv6 Router Advertisement Option for DNS Configuration",

RFC 5006, September 2007.

[RFC5226]  Narten, T. and H. Alvestrand, "Guidelines for Writing an

IANA Considerations Section in RFCs", BCP 26, RFC 5226,

May 2008.

Authors' Addresses

Benoit Lourdelet

Cisco Systems, Inc.

Village ent. GreenSide, Bat T3,

400, Av de Roumanille,

06410 BIOT - Sophia-Antipolis Cedex

France

Phone: +33 4 97 23 26 23

Email: blourdel@cisco.com

Lourdelet, et al.      Expires September 15, 2011              [Page 12]

Internet-Draft             RADIUS IPv6 Access                 March 2011

Wojciech Dec (editor)

Cisco Systems, Inc.

Haarlerbergweg 13-19

Amsterdam , NOORD-HOLLAND 1101 CH

Netherlands

Email: wdec@cisco.com

Behcet Sarikaya

Huawei USA

1700 Alma Dr. Suite 500

Plano, TX

US

Phone: +1 972-509-5599

Email: sarikaya@ieee.org

Glen Zorn

Network Zen

1310 East Thomas Street

Seattle, WA

US

Email: gwz@net-zen.net

David Miles

Alcatel-Lucent

L3 / 215 Spring St

Melbourne, Victoria 3000,

Australia

Phone:

Fax:

Email: David.Miles@alcatel-lucent.com

URI:

Lourdelet, et al.      Expires September 15, 2011              [Page 13]