Internet Research Task Force                                  T. Li, Ed.

Internet-Draft                                       Cisco Systems, Inc.

Intended status: Informational                            April 11, 2007

Expires: October 13, 2007

Design Goals for Scalable Internet Routing

draft-irtf-rrg-design-goals-00

Status of this Memo

By submitting this Internet-Draft, each author represents that any

applicable patent or other IPR claims of which he or she is aware

have been or will be disclosed, and any of which he or she becomes

aware will be disclosed, in accordance with Section 6 of BCP 79.

Internet-Drafts are working documents of the Internet Engineering

Task Force (IETF), its areas, and its working groups.  Note that

other groups may also distribute working documents as Internet-

Drafts.

Internet-Drafts are draft documents valid for a maximum of six months

and may be updated, replaced, or obsoleted by other documents at any

time.  It is inappropriate to use Internet-Drafts as reference

material or to cite them other than as "work in progress."

The list of current Internet-Drafts can be accessed at

http://www.ietf.org/ietf/1id-abstracts.txt.

The list of Internet-Draft Shadow Directories can be accessed at

http://www.ietf.org/shadow.html.

This Internet-Draft will expire on October 13, 2007.

Copyright Notice

Copyright (C) The IETF Trust (2007).

Abstract

It is commonly recognized that the Internet routing and addressing

architecture is facing challenges in scalability, mobility, multi-

homing, and inter-domain traffic engineering.  The RRG is designing

an alternate architecture to meet these challenges.  This document

consists of a prioritized list of design goals for the architecture.

Li                      Expires October 13, 2007                [Page 1]

Internet-Draft                Design Goals                    April 2007

Table of Contents

1.  Introduction  . . . . . . . . . . . . . . . . . . . . . . . . . 3

1.1.  Requirements Language . . . . . . . . . . . . . . . . . . . 3

1.2.  Priorities  . . . . . . . . . . . . . . . . . . . . . . . . 3

2.  General Design Goals Collected from Past  . . . . . . . . . . . 3

3.  Design Goals for A New Routing Architecture . . . . . . . . . . 4

3.1.  Improved routing scalability  . . . . . . . . . . . . . . . 4

3.2.  Scalable support for traffic engineering  . . . . . . . . . 4

3.3.  Scalable support for multi-homing . . . . . . . . . . . . . 4

3.4.  Scalable support for mobility . . . . . . . . . . . . . . . 4

3.5.  Simplified renumbering  . . . . . . . . . . . . . . . . . . 5

3.6.  Decoupling location and identification  . . . . . . . . . . 5

3.7.  First-class elements  . . . . . . . . . . . . . . . . . . . 6

3.8.  Routing quality . . . . . . . . . . . . . . . . . . . . . . 6

3.9.  Routing security  . . . . . . . . . . . . . . . . . . . . . 6

3.10. Deployability . . . . . . . . . . . . . . . . . . . . . . . 6

4.  IANA Considerations . . . . . . . . . . . . . . . . . . . . . . 7

5.  Security Considerations . . . . . . . . . . . . . . . . . . . . 7

6.  References  . . . . . . . . . . . . . . . . . . . . . . . . . . 7

6.1.  Normative References  . . . . . . . . . . . . . . . . . . . 7

6.2.  Informative References  . . . . . . . . . . . . . . . . . . 7

Author's Address  . . . . . . . . . . . . . . . . . . . . . . . . . 7

Intellectual Property and Copyright Statements  . . . . . . . . . . 9

Li                      Expires October 13, 2007                [Page 2]

Internet-Draft                Design Goals                    April 2007

1.  Introduction

It is commonly recognized that the Internet routing and addressing

architecture is facing challenges in scalability, mobility, multi-

homing, and inter-domain traffic engineering.  The Routing Research

Group aims to design an alternate architecture to meet these

challenges.  This document presents a prioritized list of design

goals for the architecture.

These goals should be taken as guidelines for evaluating possible

architectural solutions.  The expectation is that these goals will be

applied with good judgment.

1.1.  Requirements Language

The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT",

"SHOULD", "SHOULD NOT", "RECOMMENDED", "MAY", and "OPTIONAL" in this

document are to be interpreted as described in RFC 2119 [RFC2119].

1.2.  Priorities

Each design goal in this document has been assigned a priority, which

is one of 'required', 'strongly desired', 'desired', and 'optional'.

Required:  The solution is REQUIRED to support this goal.

Strongly desired:  The solution SHOULD support this goal unless there

exist compelling reasons showing it is unachievable,

extremely inefficient, or impractical.

Desired:  The solution SHOULD support this goal.

Optional:  The solution MAY support this goal.

It is possible that two design goals at the same priority level may

be found to be in conflict with one another.  If and when this

happens, one of them may be subsequently re-prioritized to have the

two in different priority levels.

2.  General Design Goals Collected from Past

RFC 1958 [RFC1958] provides an excellent list of the original

architectural principles of the Internet.  We incorporate them here

by reference, as part of our desired design goals.

Li                      Expires October 13, 2007                [Page 3]

Internet-Draft                Design Goals                    April 2007

3.  Design Goals for A New Routing Architecture

3.1.  Improved routing scalability

Long experience with inter-domain routing has shown us that the

global BGP routing table is continuing to grow rapidly [BGPGrowth].

Carrying this large amount of state in the routing plane is expensive

and places undue cost burdens on network participants that do not

necessarily get value from the increases in the routing table size.

Thus, the first required goal is to provide significant improvement

to the scalability of the routing plane.

3.2.  Scalable support for traffic engineering

Traffic engineering is the capability of directing traffic along

paths other than those that would be computed by normal IGP/EGP

routing.  Inter-domain traffic engineering today is frequently

accomplished by injecting more-specific prefixes into the global

routing table, which results in a negative impact on routing

scalability.  A scalable solution for inter-domain traffic

engineering is strongly desired.

3.3.  Scalable support for multi-homing

Multi-homing is the capability of an organization to be connected to

the Internet via more than one other organization.  The current

mechanism for supporting multi-homing is to let the organization

advertise one or multiple prefixes into the global routing system,

again resulting in a negative impact on routing scalability.  More

scalable solutions for multi-homing are strongly desired.

3.4.  Scalable support for mobility

Mobility is the capability of a host, network, or organization to

change its topological connectivity with respect to the remainder of

the Internet, while continuing to receive packets from the Internet.

Existing mechanisms to provide mobility support include (1)

renumbering the mobile entity as it changes its topological

attachment point(s) to the Internet; (2) renumbering and creating a

tunnel from the entity's new topological location back to its

original location; and (3) letting the mobile entity announce its

prefixes from its new attachment point(s).  The first approach alone

is considered unsatisfactory as the change of IP address may break

existing transport or higher level connections for those protocols

using IP addresses as identifiers.  The second requires the

deployment of a 'home agent' to keep track of the mobile entity's

current location and adds overhead to the routers involved, as well

as adding stretch to the path of inbound packet.  Neither of the

Li                      Expires October 13, 2007                [Page 4]

Internet-Draft                Design Goals                    April 2007

first two approaches impacts the routing scalability.  The third

approach, however, injects dynamic updates into the global routing

system as the mobile entity moves.  Mechanisms that help to provide

more efficient and scalable mobility support are desired, especially

when they can be coupled with security and support topological

changes at a high-rate.

3.5.  Simplified renumbering

Today many of the end-sites receive their IP address assignments from

their Internet Service Providers (ISP).  When such a site changes

providers, for routing to scale, the site must renumber into a new

address block assigned by its new ISP.  This can be costly, error-

prone and painful.  Automated tools, once developed, are expected to

provide significant help in reducing the renumbering pain.  It is not

expected that renumbering will be wholly automated, as some manual

reconfiguration is likely to be necessary for changing the last-mile

link.  However, the overall cost of this transition should be

drastically lowered.

In addition to being configured into hosts and routers, where

automated renumbering tools can help, IP addresses are also often

used for other purposes such as access control lists.  They are also

sometimes hard-coded into applications used in environments where

failure of the DNS could be catastrophic (e.g. certain remote

monitoring applications).  Although renumbering may be considered a

mild inconvenience for some sites, and guidelines have been developed

for renumbering a network without a flag day [RFC4192], for others,

the necessary changes are sufficiently difficult so as to make

renumbering effectively impossible.  It is strongly desired that a

new architecture allow end-sites to change providers without this

painful event.

Comment: “without this painful event” sounds subjective. To clarify, please replace “end-sites to change providers without this painful event.” with either

(a) “some end-sites should be allowed selectively to change providers without requiring renumbering.”

or,

(b) “end-sites should be allowed to change providers (with renumbering) but consideration should be given to minimizing the disruptive impact of the transition.”

3.6.  Decoupling location and identification

Numerous sources have noted that an IPv4 address embodies both host

attachment point information and identification information.  This

overloading has caused numerous semantic collisions that have limited

the flexibility of the Internet architecture.  Therefore, it is

desired that a solution separate the host location information

namespace from the identification namespace.

Caution must be taken here to clearly distinguish the decoupling of

host location and identification information, and the decoupling of

end-site addresses from globally routable prefixes; the latter has

been proposed as one of the approaches to a scalable routing

architecture.  Solutions to both problems, i.e. (1) the decoupling of

host location and identification information and (2) a scalable

Li                      Expires October 13, 2007                [Page 5]

Internet-Draft                Design Goals                    April 2007

global routing system (whose solution may, or may not, depend on the

second decoupling) are needed and it is required that their solutions

are compatible with each other.

3.7.  First-class elements

If a solution makes use of a mechanism, it is strongly desired that

the mechanism be a first-class element in the architecture

[FirstClass].  More specifically, if a tunneling mechanism is used to

provide network layering, connectivity virtualization, or a

connection-oriented mode, then it is strongly desired that the

tunneling mechanism be a first-class element in the architecture.

3.8.  Routing quality

The routing subsystem is responsible for computing a path from any

point on the Internet to any other point in the Internet.  The

quality of the routes that are computed can be measured by a number

of metrics. A comprehensive list of performance matrices and evaluation scenarios is needed and can be perhaps fully addressed in a companion I-D or annex to this document. Broadly the performance criteria would include metrics such as route quality and stability, robustness, scaling, control-plane load, inter-domain mobility optimization, etc.

Just to stimulate further thinking, we mention here some metrics that seem to be obvious for the problem space that is in consideration. These are table-size reduction ratio (TSRR), convergence time, and stretch (of path length). To evaluate the metrics, a reference AS-level topology should be defined together with appropriate service provider policies (see [JSAC-NS06] for example). The baseline performance metrics would be those for the current BGP routing over the reference topology. The TSRR is the ratio of the size of the routing table for a proposed architecture over that of the current BGP routing (for the reference topology). Comparisons can be made for all the metrics of interest between new addressing/routing architectures and those for the baseline case.

The stretch of a routing scheme is the maximum ratio of the length

of the routing path, on which a packet is delivered, to the length

of the shortest path from the source to the destination node, over

all source-destination pairs [PODC06]. Besides the maximum ratio, it would also be of interest to compute the average and the CDF of the ratio that characterizes the stretch. The CDF of the ratio would be in the form of the percentage of source-destination pairs that experience stretch less or equal to x% (x = 0% to 100% in increments of 10%).

To estimate the convergence time, a suitable reference perturbation from the steady state of the routing state can be defined. The perturbation can be in the form of restarts of some selected routers or perhaps some TCP resets that would induce BGP resets on selected peering links. The routing state re-convergence time should be measured for each of the proposed addressing/routing architectures over the reference topology under the reference perturbation condition.

[Editor's Note: A better definition of stretch, or a better

reference would be much appreciated.]

A solution is strongly desired to provide routing quality equivalent

to what is available today or better.

3.9.  Routing security

Currently, the routing subsystem is secured through a number of

protocol specific mechanisms of varying strength and applicability.

Any new architecture is required to provide at least the current

level of security. Given that working groups such as RPSEC and SIDR have already identified systemic security weaknesses in the current system, the routing security for any proposed new architectures should extend beyond the current level. It should be noted that the current state of the art in routing protocol security would advance by the time of deployment of a new solution for addressing/routing. For example, the security solutions from SIDR WG efforts in the IETF will likely progress to RFCs and could be already in deployment in this time frame.

3.10.  Deployability

Since solutions that are not deployable are simply academic

exercises, solutions are required to be deployable.  Furthermore,

given the extensive deployed base of today's Internet, a solution is

required to be incrementally deployable.

Li                      Expires October 13, 2007                [Page 6]

Internet-Draft                Design Goals                    April 2007

4.  IANA Considerations

This memo includes no requests to IANA.

5.  Security Considerations

All solutions are required to provide security that is at least as

strong as the existing Internet routing and addressing architecture.

6.  References

6.1.  Normative References

[RFC1958]  Carpenter, B., "Architectural Principles of the Internet",

RFC 1958, June 1996.

[RFC2119]  Bradner, S., "Key words for use in RFCs to Indicate

Requirement Levels", BCP 14, RFC 2119, March 1997.

[RFC4192]  Baker, F., Lear, E., and R. Droms, "Procedures for

Renumbering an IPv6 Network without a Flag Day", RFC 4192,

September 2005.

6.2.  Informative References

[BGPGrowth]

Huston, G., "BGP Routing Table Analysis Reports",

<http://bgp.potaroo.net/>.

[FirstClass]

"First-class object",

<http://en.wikipedia.org/wiki/First-class_object>.

[PODC06]   Konjevod, G., Andrea, R., and D. Xia, "Optimal-Stretch

Name-Independent Compact Routing in Doubling Metrics",

<http://www.public.asu.edu/~dxia2/papers/PODC06.pdf>.

[JSAC-NS06]   K. Sriram, D. Montgomery, O. Borchert, O. Kim, and D.R. Kuhn, 
"Study of BGP Peering Session Attacks and Their Impacts on Routing Performance," 
IEEE Journal on Selected Areas in Communications: Special issue on High-Speed Network Security, Vol. 24, No. 10, October 2006, pp. 1901-1915.

Li                      Expires October 13, 2007                [Page 7]

Internet-Draft                Design Goals                    April 2007

Author's Address

Tony Li (editor)

Cisco Systems, Inc.

425 East Tasman Dr.

San Jose, CA  95134

USA

Phone: +1 408 853 1494

Email: tli@cisco.com

Li                      Expires October 13, 2007                [Page 8]

Internet-Draft                Design Goals                    April 2007

Full Copyright Statement

Copyright (C) The IETF Trust (2007).

This document is subject to the rights, licenses and restrictions

contained in BCP 78, and except as set forth therein, the authors

retain all their rights.

This document and the information contained herein are provided on an

"AS IS" basis and THE CONTRIBUTOR, THE ORGANIZATION HE/SHE REPRESENTS

OR IS SPONSORED BY (IF ANY), THE INTERNET SOCIETY, THE IETF TRUST AND

THE INTERNET ENGINEERING TASK FORCE DISCLAIM ALL WARRANTIES, EXPRESS

OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF

THE INFORMATION HEREIN WILL NOT INFRINGE ANY RIGHTS OR ANY IMPLIED

WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

Intellectual Property

The IETF takes no position regarding the validity or scope of any

Intellectual Property Rights or other rights that might be claimed to

pertain to the implementation or use of the technology described in

this document or the extent to which any license under such rights

might or might not be available; nor does it represent that it has

made any independent effort to identify any such rights.  Information

on the procedures with respect to rights in RFC documents can be

found in BCP 78 and BCP 79.

Copies of IPR disclosures made to the IETF Secretariat and any

assurances of licenses to be made available, or the result of an

attempt made to obtain a general license or permission for the use of

such proprietary rights by implementers or users of this

specification can be obtained from the IETF on-line IPR repository at

http://www.ietf.org/ipr.

The IETF invites any interested party to bring to its attention any

copyrights, patents or patent applications, or other proprietary

rights that may cover technology that may be required to implement

this standard.  Please address the information to the IETF at

ietf-ipr@ietf.org.

Acknowledgment

Funding for the RFC Editor function is provided by the IETF

Administrative Support Activity (IASA).

Li                      Expires October 13, 2007                [Page 9]